## Slide 1
IEEE International Parallel and Distributed Processing Symposium (IPDPS) 2020
A Study of Graph Analytics for Massive Datasets on Distributed Multi-GPUs
Vishwesh Jatala1,2, Roshan Dathathri1,3, Gurbinder Gill1,3, Loc Hoang1,3,
V. Krishna Nandivada4,5, and Keshav Pingali1,3
1The University of Texas at Austin, USA
2vishwesh.jatala@austin.utexas.edu
3{loc,roshan,gill,pingali}@cs.utexas.edu
4Indian Institute of Technology Madras, India
5nvk@iitm.ac.in

## Slide 2: Motivation
Graph Analytics
Data Growth!
  Clueweb is ~ 1 TB
42.5 B edges
Limited GPU Memory
  NVIDIA P100 has
16 GB memory
Distributed Multi-GPUs
Partition?
Compute?
Synchronize?
Images Source: Internet

## Slide 3
Identifies scope for improvements
Study of Graph Analytics on Distributed GPUs
Limitations of Prior Studies
Contributions of Our Study
Customized for few applications
Scalable BFS [Pan et al. IPDPS’18]
Not exhaustive
[Gluon PLDI’18, Lux PVLDB’17]
Restricted for single GPUs
Graph survey [Shi et al.Comput.’18]
Focused only for CPUs
Partitioning study [Gill et al. PVLDB’18 ]
Shows impact of partitioning, computation, and communication
Provides key suggestions
for designers
Analyzes massive graphs using state-of-the-art D-IrGL
3

## Slide 4: Distributed Graph Analytics
GPU1
Device Memory
GPU2
Device Memory
Memory
CPU
Network
Node1
Node2
Input Graph G
G1
G2
G3
G4
Partition Graph
(2) Compute
(3) Synchronize
GPU3
Device Memory
GPU4
Device Memory
Memory
CPU

## Slide 5: Evaluated Techniques in The Study
Partitioning
Computation
Synchronization
CuSP [Hoang et al. IPDPS’19]
Incoming Edge Cut1,2 (IEC)
Outgoing Edge Cut2,3 (OEC)
Cartesian Vertex Cut2,4 (CVC)
Hybrid Vertex Cut5 (HVC)
Thread/Warp/CTA Distribution3,6,7 (TWC)
Adaptive Load Balancer (ALB)8
Execution Model
  Bulk-Synchronous Parallel1,2,9 (BSP)
  Bulk-Asynchronous Parallel10 (BASP)
1Lux PVLDB’17, 2Gluon PLDI’18, 3Gunrock IPDPS’17, 4Boman et al. SC’13, 5PowerLyra EuroSys’ 15, 6IrGL OOPSLA’16,
7Merill et al. PPOPP’12, 8Jatala et al. Arxiv’19, 9Valiant CACM’90, 10Gluon-Async PACT’19,
Communication
  Update-Only2
  All-Shared1

## Slide 6: Experimental Setup
Inputs (Medium) | ¦V¦ | ¦E¦ | Input (Large) | ¦V¦ | ¦E¦
twitter50 | 51 M | 1,963 M | clueweb12 | 978 M | 42.5 B
friendster | 66 M | 1,806 M | uk14 | 788 M | 47.6 B
uk07 | 106 M | 3,739 M | wdc14 | 1725 M | 64.4 B
bfs, sssp, cc, pagerank, and kcore
Benchmarks
Inputs
Bridges Supercomputer
32 (machines) * 2 (NVIDIA P100 GPUs)
Hardware
D-IrGL and Lux (Distributed Multi-GPU Frameworks)
Frameworks

## Slide 7: Results: Computation and Synchronization
Variant | Optimizations
Var1 | TWC + All Shared + Sync
Var2 | ALB + All Shared + Sync
Var3 | ALB + Update Only + Sync
Var4 (default) | ALB + Update Only + Async
All variants (even Lux) use same partitioning policy (IEC).

## Slide 8: Analyzing Computation and Synchronization
Host-device time is significant
Asynchronous behavior should be throttled
32 GPUs
64 GPUs
Notes: 32 P100 GPUs

## Slide 9: Analyzing Partitioning Schemes
CVC outperforms other schemes
on 16 or more GPUs
  fewer communication partners
Static load imbalance not correlated to dynamic load imbalance
Static load imbalance is correlated to memory usage
  Critical for GPUs due to limited memory

## Slide 10: Conclusion
Detailed analysis of distributed multi-GPU graph analytics
Lessons:
  CVC is crucial for scaling
  Static load balance is important for GPUs
Scope for Improvements:
  Reduce host-device communication time through GPUDirect
  Control asynchrony in Bulk-Asynchronous execution
Please contact authors for any questions. Thank you!